## Slide 1: OLFOSENSE Instrumental Odor Monitoring System

## Slide 2
Multi-parameter
Odor (Olfactometric Units - OUE/m3)
Total VOC (ppb)
NH3 & H2S (ppb)
PM10 - PM2.5 - PM1 (µg/m3)
Weather parameters
Dispersion modeling

## Slide 3
Gateway UMTS Data local storage
Module MOS PID 2XECD
Charcoal filter Zero air

## Slide 4
Odor Measurement
ODOR UNITS / m3
Dynamic Olfactometry
OlfoSense MOS Array
Prediction
Metal Oxide Semiconductors
Standard algorithm
(nbutanol gas)

## Slide 5
Calibration for Odor measurement
Prediction
On-site algorithm
On-site samples
OU / m3

## Slide 6
VOC Measurement
RANGE: 5 ppb - 20 ppm
CAPABILITY: ̴320 compounds
CALIBRATION: Isobutylene
PID (PhotoIonization Detector) 10.6 eV

## Slide 7
H2S - NH3 measurements
Electrochemical cell
RANGE: H2S = 5 ppb – 50 ppm NH3 = 5 ppb – 100 ppm
CALIBRATION: NH3 - H2S
S compounds = petrochemical / anaerobic plants
Ammonia = aerobic plants

## Slide 8
Data Management
Remote Control
Gateway: GPRS/UMTS
Cloud Server
OlfoClient platform
Local Storage
SD card

## Slide 9
OlfoSense Network
Database
Web Services
OLFOCLIENT
CLOUD
OLFOSENSE

## Slide 10
OlfoClient platform

## Slide 11
OlfoClient
Secure access

## Slide 12
OlfoClient
Real-time overview
Live data

## Slide 13
OlfoClient
Historical data: charts and tables
Select a device
Select a date
or date range

## Slide 14
OlfoClient
Interactive analytics
Printable reports

## Slide 15
OlfoClient
ALARM
Device | Parameter | Rule | Limit (ppb)
Olfo 182 | OU | > | 800
Olfo 179 | VOC | > | 2500

## Slide 16
SMIT Olfo Dispersion Modeling

## Slide 17
FEATURES
Input
ISC Aermod (US–EPA) dispersion model
Fallout plume of odorous compounds
Impact on sensitive receptors
Real-time impact assessment
OU/m3
Weather data
Terrain data
Process parameters (elevation from the ground, odor emission rate, temperature…)

## Slide 20
Odor complaints management

## Slide 21
CASE HISTORY
Landfill of hazardous industrial waste
GOALS
Odor / H2S continuous monitoring
Dispersion plume true extent
Prompt intervention: facility staff + firefighters
Facts
Area: 6.60 hectares
6 sensitive receptors (houses + hospital)
Horography: flat land
Next to the highway
OlfoSense network:
1 unit deployed on the main odor source
2 units on perimeter
1 unit at the nearest downwind receptor

## Slide 22
CASE HISTORY
Petrochemical plant
GOALS
Pinpoint the main sources within the facility & carry out plant improvements (fix up tanks covers)
Dispersion plume true extent
Prompt intervention
Facts
Refinery area: 212 hectares
82 tanks of crude oil and finished products
1 receptor (the city - 48000 citizens)
Long-standing dispute with the community over offensive odors
OlfoSense network:
4 units deployed on a few run-down tanks
2 units on downwind perimeter
1 unit in the city area